## Slide 1: Session Analog to Digital Convertor
By : Ahmad Hazem

## Slide 2: ADC pinout
PORTA in the atmega32 consists of 8 channels, allowing up to 8 peripherals to be connected to the microcontroller.

## Slide 3
Conversion Time : Conversion Time is the time taken by the ADC to convert the analog input into a binary digital input. The conversion time is dictated according to the clock frequency connected to it. Also, it can be called the sampling time.
Vref : It is the input voltage used as a reference voltage for the ADC

## Slide 4
Resolution :
The ADC in the atmega32 has a 10-bit resolution. The ADC resolution is defined as the smallest incremental voltage that can be recognized and thus causes a change in the digital output. It is expressed as the number of bits output by the ADC.
Formula to calculate resolution is

## Slide 5: Atmega32 ADC features
10-bit Resolution
13 µs - 260 µs Conversion Time
8 Multiplexed Single Ended Input Channels
7 Differential Input Channels
2 Differential Input Channels with Optional Gain of 10x and 200x
Optional Left adjustment for ADC Result Readout
0 - VCC ADC Input Voltage Range
Selectable 2.56V ADC Reference Voltage
Free Running or Single Conversion Mode
ADC Start Conversion by Auto Triggering on Interrupt Sources
Interrupt on ADC Conversion Complete

## Slide 6: ADCH/ADCL (ADC data register)
It is a 10-bit register composed of 2 8-bit registers. One register holds the LSB 8-bit in it (ADCL for an example), and the other register holds the MSB 2-Bit in it (ADCH for example).

## Slide 7: ADMUX Register
Bit 7: 6 – REFS1 : 0: Reference Selection Bits
Reference voltage selection for ADC
REFS1 | REFS0 | Description
0 | 0 | AREF pin
0 | 1 | AVCC pin i.e. Vcc 5 V
1 | 0 | Reserved
1 | 1 | Internal 2 (2.56 V)

## Slide 8: ADMUX Register
Bit 5 – ADLAR: ADC Left Adjust Result
Use 10-bits output as upper bits or lower bits in ADCH & ADCL.

## Slide 9: ADMUX Register
Bits 4 : 0 – MUX4 : 0: Analog Channel and Gain Selection Bits
We can select input channel ADC0 to ADC7 by using these bits.
Selecting a channel is very easy, just put the channel number in MUX4 : 0.
Suppose you are connecting the input to ADC channel 2 then put 00010 in MUX4 : 0.
Suppose you are connecting the input to ADC channel 5 then put 00101 in MUX4 : 0.

## Slide 11: ADCSRA Register
Bit 7 – ADEN: ADC Enable
Writing one to this bit enables the ADC. By writing it to zero, the ADC is turned off. Turning the ADC off while a conversion is in progress, will terminate this conversion.
Bit 6 – ADSC: ADC Start Conversion
Writing one to this bit starts the conversion.
Bit 5 – ADATE: ADC Auto Trigger Enable
Writing one to this bit, results in Auto Triggering of the ADC is enabled.
Bit 4 – ADIF: ADC Interrupt Flag
This bit is set when an ADC conversion completes, and the Data Registers are updated.
Bit 3 – ADIE: ADC Interrupt Enable
Writing one to this bit, the ADC Conversion Complete Interrupt is activated.

## Slide 12: ADCSRA Register
Bits 2 : 0 – ADPS2 : 0: ADC Pre-scaler Select Bits
These bits determine the division factor between the XTAL frequency and the input clock to the ADC
ADPS2 | ADPS1 | ADPS0 | Description
0 | 0 | 0 | 2
0 | 0 | 1 | 2
0 | 1 | 0 | 4
0 | 1 | 1 | 8
1 | 0 | 0 | 16
1 | 0 | 1 | 32
1 | 1 | 0 | 64
1 | 1 | 1 | 128
Note frequency the atmega32 can support for conversion rate is 50kHz to 200KHz so , when using the internal clock of the atmega32 (16MHz) we always use the pre-scale of 128, unless an external is oscillator is connected.

## Slide 14: SFIOR register (Special Function input output register)
Bits 7,6,5 : ADTS2, ADTS1, ADTS0:
The ADTSn bit are trigger bits for the ADC to convert the analogue voltage strobed on the ADC channel pin into a decimal value stored in the ADCH/ADCL data register.
ADTS2 | ADTS1 | ADTS0 | Description
0 | 0 | 0 | Free Running mode
0 | 0 | 1 | Analog Comparator
0 | 1 | 0 | External Interrupt Request 0
0 | 1 | 1 | Timer/Counter0 Compare Match
1 | 0 | 0 | Timer/Counter0 Overflow
1 | 0 | 1 | Timer/Counter1 Compare Match B
1 | 1 | 0 | Timer/Counter1 Overflow
1 | 1 | 1 | Timer/Counter1 Capture Event

## Slide 15: LM35 Temperature sensor
Write an AVR c code to interface LM35 with atmega32. when temperature is more than 50 degree Celsius, make a LED connected to port C pin 0 go on;
Create a fire alarm system using LM35 temperature system, IR flame sensor, LCD , buzzer, LED. Display temperature, gas sensor on the LCD . If temperature is above 50 ,and flame is detected set buzzer on , and LED to flicker

## Slide 16: Interrupts

## Slide 17: Interrupts (Exceptions handling by CPU)
Exceptions
Hardware (External interrupts - RESET)
Software (Division by zero – stack overflow)

## Slide 18: Reset circuit and watch dog timer
Watch Dog Timer :
Counter that count time period for each function .If function took more than calculated time period, an automatic reset occurs.
RESET
Hardware
Watch dog timer
External Interrupt
Software

## Slide 23: Definitions:
Interrupt latency: Time between interrupt happens and context switching start
Interrupt response time : Time between Interrupt happens and ISR function start running.
Interrupt Recovery : Time between interrupts and context switching finish
Interrupt Process Time : Time between interrupts happens and the returning of the main function

## Slide 24: External Interrupts

## Slide 25: GICR Registers
Bit 7 – INT1: External Interrupt Request 1 Enable
0: Disable external interrupt
1: Enable external interrupt
Bit 6 – INT0: External Interrupt Request 0 Enable
0: Disable external interrupt
1: Enable external interrupt
Bit 5 – INT2: External Interrupt Request 2 Enable
0: Disable external interrupt
1: Enable external interrupt

## Slide 26: MCU Control Register (MCUCR)

## Slide 27: MCU Control and Status Register (MCUCSR)

## Slide 28: Examples
Write an AVR c code that enables a LED when a push button is pushed using an interrupt.
Write an AVR c code interrupt code when a button is pushed in the keypad , the letter appears on the LCD